## Slide 1: Extended Spectrum DOCSIS: A Pragmatic Approach Arttu Purmonen, Vice President

## Slide 2: Decade after decade
600 MHz
860 MHz
1 GHz
1.2 GHz
1.8 GHz

## Slide 3: Decade after decade - From changes to solutions
Changes
More bits/symbol requiring better MER
Higher frequencies and loads, requiring better amplifiers
Lower margins due to higher Total Composite Power (TCP)
Solutions
More robust modulation methods and FECs
Better amplifiers
Digital fibre instead of analog (shift to DAA)
Careful network planning and intelligent amplifiers

## Slide 4: Decade after decade – A challenge of continuity
What has NOT changed
  Engineers complaining that the next change is ”different”
  Distances between existing street cabinets
Solutions
  Time
  Better amplifiers and careful network planning
Questions
  How good are these better amplifiers going to be?
  Are booster amplifiers needed between street cabinets?

## Slide 5: If distance between amplifiers is chosen without restraints
Cascading 1.8 GHz amplifiers and reaching 4K QAM can be ”trivial”
Theoretically calculated and measured results follow the 10log equation
In practice some of these amplifiers would be trunk extenders in new locations
RPD
≈0.1 dB/m @ 1.8 GHz
24 dB@1.8GHz
240 m
240 m
240 m
240 m
24 dB
24 dB
24 dB
24 dB
MER 50 dB
MER 48 dB
CNR 60 dB

## Slide 6: If distance between street cabinets is more challenging
Cascading 1.8 GHz amplifiers and reaching 4K QAM can be difficult
Theoretically calculated and measured results do not follow 10log (closer to 13log)
RPD
48 dB@1.8GHz
480 m
480 m
48 dB
48 dB
≈0.1 dB/m @ 1.8 GHz
MER 50 dB
MER 38 dB
CNR 45 dB @ 1.8 GHz

## Slide 7: Cascades & MER
Attenuation
between
amps ≈ gain
@1.8 GHz
Number of amps
Gain
50 dB
25 dB
2
32
1

## Slide 8: Cascades & MER
Attenuation
between
amps ≈ gain
@1.8 GHz
Number of amps
4K OFDM
2K OFDM
1K OFDM
TCP≈70 dBmV
Gain
50 dB
25 dB
2
32
1

## Slide 9: Summary
2. Attenuation between amplifiers guides 1.8 GHz network upgrades
1. Coax has served us well, all challenges have been solved wave by wave
3. Today, 1.8 GHz amplifiers can manage 70 dBmV TCP
4. Careful network planning and precise adjustments reduce number of new locations
  The accuracy of signal levels becomes paramount
  -> Intelligent and automatic adjustments secure proper network operation
9
THANKS, contact: arttu.purmonen@teleste.com